Worksheet 3.2 - Torque

- What force F1 is needed to balance the beam in the diagram below?

- How far from the pivot must the 64 N object be placed to balance the beam in the diagram below?

- What upward force F1 is needed to chaieve rotational equilibrium in the diagram below?

- If the torque needed to loosen a lug nut is 45 Nm and you are using a 35 cm wheel wrench, what force do you need to exert perpendicular to the end of the wrench?

- A beam of negligible mass is attached to a wall by a hinge.  Attached to the center of the beam is a 400 N weight.   A rope supports the beam as shown in the diagram.  What is the tension in the rope?

- Two students sit on either end of a uniform teeter-totter. Student 1 sits 1.10 m from the pivot while Student 2 sits 0.85 m from the pivot.  If Student 1 has a mass of 72 kg, what is the mass of Student 2?

- A 0.75 kg bird stands on a uniform 1.0 kg stick as shown. The stick is attached to a wall with a hinge and to the ceiling with a rope of negligible mass.  What is the tension in the rope?

- Two masses (m1 = 3.00 kg, m2 = 5.00 kg) hang from the ends of a metre stick as shown.  If the mass of the metre stick is negligible, at what distance from the left of the metre stick should a pivot be placed so that the system will be balanced?

- A uniform 400 N diving board is supported at two points as shown in the diagram.  If a 75 kg diver stands at the end of the board, what are the forces acting on the each support?

- A 650 N student stands on a 250 N uniform beam that is supported by two supports as shown in the diagram.  If the supports are 5.0 m apart and the student stands 1.5 m from the left support:

a) What is the force that the right support exerts on the beam?

b) What is the force that the left support exerts on the beam?

Answers:

- (5.3 N)

- (37 cm OR 0.37 m)

- 6.1 x 102 N

- (130 N)

- (200 N)

- (93 kg)

- (10. N)

- (0.625 m)

- (left support = 2.61x103 N down , right support = 3.74x103 N up)

- Fright = 320 N , Fleft = 580N

# Text boxes

400 N

T

1.2 m

0.90 m

m1

m2

2.0 m

0.50 m

5.0 m

1.5 m