Worksheet 6.4 - Rotation Angle, Angular Velocity and Angular Acceleration

- A wheel rotates 3 times.  What is its angular displacement?

- If a 30 cm radius wheel rotates through 3 radians how far has it rolled?

- What is the angular displacement of the minute hand on a clock during a 30-minute interval.

- Three hours pass by.  What is the angular displacement of the Hour hand on the clock during this interval?

- A carnival ride rotates through 4 radians of angular displacement.  If the ride has a diameter of 4 meters, what is the path length that the passengers have moved in this time?

- A merry-go-round rotates 10 complete revolutions.  What path length has the passenger moved through if they are seated 2 meters from the ride’s center?

- Through how many radians has a 40 cm radius wheel rotated through if it has traveled 10 meters?

- A motor runs at 1200 rpm.  What is the angular speed of the motor?

- A wheel is observed to rotate 5 complete revolutions in 25 seconds.  What is its angular speed?

- What is the angular speed of the minute hand of any clock?

- What is the tangential velocity of a point at the equator of the earth?  (radius of earth = 6.37 x 106 meters)

- What is the angular velocity of a point at the equator of the earth?  (radius of earth = 6.37 x 106 meters)

- An automobile wheel rotates at 500 rpm.

  - If the wheel has a diameter of 1.0 meter, what is the velocity (m/s) of the automobile?

  - If the wheel is underinflated, its diameter is only 0.90 meters and rotates at the same speed.  What velocity will the car have?

- In order to travel at 20.0 m/s what angular speed must your tires have if your tires have a 0.80 m radius?

- A cyclist traveling at 5.0 m/s uniformly accelerates up to 10. m/s in 2.0 seconds.  Each tire of the bike has a 35 cm radius, and a small pebble is caught in the tread of one of them. What is the angular acceleration of the pebble during those two seconds?

- A flywheel speeds up uniformly from rest to 900 rpm in 2 minutes.

  - Find the angular acceleration.

  - Find the tangential acceleration of the rim if the flywheel has a 0.50 m radius.

- A CD player spins at 8590 rpm. If it starts from rest and has an acceleration of 450 rad/s2, how long does it take to reach full speed?

Answers:

- 1080o or 18.85 rads

- 90 cm

- π radians 3.14… radians

- 1.57 radians

- 8 m

- 125.5 m

- 25 radians

- 126 rad/s

- 1.3 rad/s

- 0.10 rad/s

- 4.63 x 102 m/s

- 7.27 x 10-5 rad/s

- a. 26 m/s b. 21 m/s

- 25 rads/s

- 7.14 rad/s2

- a. 0.785 rad/s2 b. 0.393 m/s2

- 2.0 s