You will need to be able to solve torque, angular acceleration, and angular kinematics problems and be able to apply angular work and momentum to these problems.

Force = ma 				τ = I.α

p = F.t                                      	L= τ.t

- There are two spheres of the same diameter, but one has twice the mass of the other.  How much larger is the larger sphere’s moment of inertia? (Isphere = 2/5 mr2)

- A wheel has a moment of inertia of 3.00 kg m2.  It is subjected to a 3.50 N m of torque.  What angular acceleration does it experience?

- Mr. Henning’s pottery wheel has angular velocity of 15 rad/sec.  Then Mr. Henning begins to use his hands to form the clay into a beautiful vase.  The friction between the clay and his hands is 2.00 N.  The clay has a radius of .15 m and the wheel with clay has a moment of inertia of .11 kg m2.

  - What is the torque produced on the clay and wheel by the friction from Mr. Henning’s hands?

  - How much time will it take for the clay and wheel to stop spinning? (ɷ=ɑt)

- A rope is wrapped around a solid cylinder of mass 10 kg with a radius of 1.5 m.  What is the angular acceleration of the cylinder if a force of 5.00 N is applied parallel to the edge of the wheel? (Idisk = ½ mr2)

- Chris’ rad bicycle wheel has a radius of 38 cm and is given an angular acceleration of 2.67 rad/s2 by applying a force of 0.35 N on the edge of the wheel.  What is the wheel’s moment of inertia?

- A toy top has a rod with a diameter of 8.0 mm and a disk of mass 0.0125 kg and diameter of 3.5 cm.  The moment of inertia of the rod can be neglected.  The top is spun in 0.50 s by wrapping a string around the rod and pulling it from rest to a velocity of 3.0 m/s.What is the resulting angular acceleration of the top? (a=ɑr)

- A seesaw is made from a 5.0 meter long 56.0 kg rod of uniform mass distribution which rests on a fulcrum located in the center of the rod.  If a 42 kg child sits so that his center of mass is located 2.20m away from the pivot point,

  - What is the moment of inertia of the seesaw and child? (Irod=1/12mL2)

  - How much torque would be needed to cause an angular acceleration of 0.15 rad/s2

# Text boxes

Answers: (1) Twice as much, (2) 1.17 rad/s2, (3a) .30 Nm, (3b) 5.5 s,

(4) 0.67rad/s2, (5) 0.050 kgm2, (6) 1500 rad/s, (7a) 320 kgm2, (7b) 48. Nm